## Slide 1: Mobile Communications Chapter 7: Wireless LANs
Characteristics
IEEE 802.11 (PHY, MAC, Roaming, .11a, b, g, h, i, n … z)
Bluetooth / IEEE 802.15.x
IEEE 802.16/.20/.21/.22
RFID
Comparison

## Slide 2: Mobile Communication Technology according to IEEE (examples)
Local wireless networks
WLAN 802.11
802.11a
802.11b
802.11i/e/…/n/…/z/aa
802.11g
WiFi
802.11h
Personal wireless nw
WPAN 802.15
802.15.4
802.15.1
802.15.2
Bluetooth
802.15.4a/b/c/d/e/f/g
ZigBee
802.15.3
Wireless distribution networks
WMAN 802.16 (Broadband Wireless Access)
[802.20 (Mobile Broadband Wireless Access)]
802.16e (addition to .16 for mobile devices)
+ Mobility
WiMAX
802.15.3b/c
802.15.5, .6 (WBAN)

## Slide 3: Characteristics of wireless LANs
Advantages
  very flexible within the reception area
  Ad-hoc networks without previous planning possible
  (almost) no wiring difficulties (e.g. historic buildings, firewalls)
  more robust against disasters like, e.g., earthquakes, fire - or users pulling a plug...
Disadvantages
  typically very low bandwidth compared to wired networks (1-10 Mbit/s) due to shared medium
  many proprietary solutions, especially for higher bit-rates, standards take their time (e.g. IEEE 802.11n)
  products have to follow many national restrictions if working wireless, it takes a vary long time to establish global solutions like, e.g., IMT-2000

## Slide 4: Design goals for wireless LANs
global, seamless operation
low power for battery use
no special permissions or licenses needed to use the LAN
robust transmission technology
simplified spontaneous cooperation at meetings
easy to use for everyone, simple management
protection of investment in wired networks
security (no one should be able to read my data), privacy (no one should be able to collect user profiles), safety (low radiation)
transparency concerning applications and higher layer protocols, but also location awareness if necessary
…

## Slide 5: Comparison: infrastructure vs. ad-hoc networks
infrastructure network
ad-hoc network
AP
AP
AP
wired network
AP: Access Point

## Slide 6: WiFi Routers

## Slide 7: 802.11 - Architecture of an infrastructure network
Station (STA)
  terminal with access mechanisms to the wireless medium and radio contact to the access point
Basic Service Set (BSS)
  group of stations using the same radio frequency
Access Point
  station integrated into the wireless LAN and the distribution system
Portal
  bridge to other (wired) networks
Distribution System
  interconnection network to form one logical network (EES: Extended Service Set) based on several BSS
Distribution System
Portal
802.x LAN
Access
Point
802.11 LAN
BSS2
802.11 LAN
BSS1
Access
Point
STA1
STA2
STA3
ESS
Notes: 9

## Slide 8: 802.11 - Architecture of an ad-hoc network
Direct communication within a limited range
  Station (STA): terminal with access mechanisms to the wireless medium
  Independent Basic Service Set (IBSS): group of stations using the same radio frequency
802.11 LAN
IBSS2
802.11 LAN
IBSS1
STA1
STA4
STA5
STA2
STA3

## Slide 9: IEEE standard 802.11
mobile terminal
access point
fixed
terminal
application
TCP
802.11 PHY
802.11 MAC
IP
802.3 MAC
802.3 PHY
application
TCP
802.3 PHY
802.3 MAC
IP
802.11 MAC
802.11 PHY
LLC
infrastructure
network
LLC
LLC

## Slide 10: 802.11 - Layers and functions
PLCP Physical Layer Convergence Protocol
  clear channel assessment signal (carrier sense)
PMD Physical Medium Dependent
  modulation, coding
PHY Management
  channel selection, MIB
Station Management
  coordination of all management functions
PMD
PLCP
MAC
LLC
MAC Management
PHY Management
MAC
  access mechanisms, fragmentation, encryption
MAC Management
  synchronization, roaming, MIB, power management
PHY
DLC
Station Management

## Slide 11: 802.11 - Physical layer (legacy)
3 versions: 2 radio (typ. 2.4 GHz), 1 IR
  data rates 1 or 2 Mbit/s
FHSS (Frequency Hopping Spread Spectrum)
  spreading, despreading, signal strength, typ. 1 Mbit/s
  min. 2.5 frequency hops/s (USA), two-level GFSK modulation
DSSS (Direct Sequence Spread Spectrum)
  DBPSK modulation for 1 Mbit/s (Differential Binary Phase Shift Keying), DQPSK for 2 Mbit/s (Differential Quadrature PSK)
  preamble and header of a frame is always transmitted with 1 Mbit/s, rest of transmission 1 or 2 Mbit/s
  chipping sequence: +1, -1, +1, +1, -1, +1, +1, +1, -1, -1, -1 (Barker code)
  max. radiated power 1 W (USA), 100 mW (EU), min. 1mW
Infrared
  850-950 nm, diffuse light, typ. 10 m range
  carrier detection, energy detection, synchronization

## Slide 12: FHSS PHY packet format (legacy)
Synchronization
  synch with 010101... pattern
SFD (Start Frame Delimiter)
  0000110010111101 start pattern
PLW (PLCP_PDU Length Word)
  length of payload incl. 32 bit CRC of payload, PLW < 4096
PSF (PLCP Signaling Field)
  data of payload (1 or 2 Mbit/s)
HEC (Header Error Check)
  CRC with x16+x12+x5+1
synchronization
SFD
PLW
PSF
HEC
payload
PLCP preamble
PLCP header
80
16
12
4
16
variable
bits

## Slide 13: DSSS PHY packet format (legacy)
Synchronization
  synch., gain setting, energy detection, frequency offset compensation
SFD (Start Frame Delimiter)
  1111001110100000
Signal
  data rate of the payload (0A: 1 Mbit/s DBPSK; 14: 2 Mbit/s DQPSK)
Service
  future use, 00: 802.11 compliant
Length
  length of the payload
HEC (Header Error Check)
  protection of signal, service and length, x16+x12+x5+1
synchronization
SFD
signal
service
HEC
payload
PLCP preamble
PLCP header
128
16
8
8
16
variable
bits
length
16

## Slide 14: 802.11 - MAC layer I - DFWMAC
Traffic services
  Asynchronous Data Service (mandatory)
    exchange of data packets based on “best-effort”
    support of broadcast and multicast
  Time-Bounded Service (optional)
    implemented using PCF (Point Coordination Function)
Access methods
  DFWMAC-DCF CSMA/CA (mandatory)
    collision avoidance via randomized „back-off“ mechanism
    minimum distance between consecutive packets
    ACK packet for acknowledgements (not for broadcasts)
  DFWMAC-DCF w/ RTS/CTS (optional)
    Distributed Foundation Wireless MAC
    avoids hidden terminal problem
  DFWMAC- PCF (optional)
    access point polls terminals according to a list

## Slide 15: 802.11 - MAC layer II
Priorities
  defined through different inter frame spaces
  no guaranteed, hard priorities
  SIFS (Short Inter Frame Spacing)
    highest priority, for ACK, CTS, polling response
  PIFS (PCF IFS)
    medium priority, for time-bounded service using PCF
  DIFS (DCF, Distributed Coordination Function IFS)
    lowest priority, for asynchronous data service
t
medium busy
SIFS
PIFS
DIFS
DIFS
next frame
contention
direct access if medium is free  DIFS

## Slide 16: 802.11 - CSMA/CA access method I
t
medium busy
DIFS
DIFS
next frame
contention window
(randomized back-off mechanism)
station ready to send starts sensing the medium (Carrier Sense based on CCA, Clear Channel Assessment)
if the medium is free for the duration of an Inter-Frame Space (IFS), the station can start sending (IFS depends on service type)
if the medium is busy, the station has to wait for a free IFS, then the station must additionally wait a random back-off time (collision avoidance, multiple of slot-time)
if another station occupies the medium during the back-off time of the station, the back-off timer stops (fairness)
slot time (20µs)
direct access if medium is free  DIFS
Notes: 12

## Slide 17: 802.11 - CSMA/CA access method II
Sending unicast packets
  station has to wait for DIFS before sending data
  receivers acknowledge at once (after waiting for SIFS) if the packet was received correctly (CRC)
  automatic retransmission of data packets in case of transmission errors
t
SIFS
DIFS
data
ACK
waiting time
other
stations
receiver
sender
data
DIFS
contention

## Slide 18: 802.11 - DFWMAC
Sending unicast packets
  station can send RTS with reservation parameter after waiting for DIFS (reservation determines amount of time the data packet needs the medium)
  acknowledgement via CTS after SIFS by receiver (if ready to receive)
  sender can now send data at once, acknowledgement via ACK
  other stations store medium reservations distributed via RTS and CTS
t
SIFS
DIFS
data
ACK
defer access
other
stations
receiver
sender
data
DIFS
contention
RTS
CTS
SIFS
SIFS
NAV (RTS)
NAV (CTS)

## Slide 19: Fragmentation
t
SIFS
DIFS
data
ACK1
other
stations
receiver
sender
frag1
DIFS
contention
RTS
CTS
SIFS
SIFS
NAV (RTS)
NAV (CTS)
NAV (frag1)
NAV (ACK1)
SIFS
ACK2
frag2
SIFS

## Slide 20: DFWMAC-PCF I (almost never used)
PIFS
stations‘
NAV
wireless
stations
point
coordinator
D1
U1
SIFS
NAV
SIFS
D2
U2
SIFS
SIFS
SuperFrame
t0
medium busy
t1

## Slide 21: DFWMAC-PCF II
t
stations‘
NAV
wireless
stations
point
coordinator
D3
NAV
PIFS
D4
U4
SIFS
SIFS
CFend
contention
period
contention free period
t2
t3
t4

## Slide 22: 802.11 - Frame format
Types
  control frames, management frames, data frames
Sequence numbers
  important against duplicated frames due to lost ACKs
Addresses
  receiver, transmitter (physical), BSS identifier, sender (logical)
Miscellaneous
  sending time, checksum, frame control, data
Frame
Control
Duration/
ID
Address
1
Address
2
Address
3
Sequence
Control
Address
4
Data
CRC
2
2
6
6
6
6
2
4
0-2312
bytes
Protocol
version
Type
Subtype
To
DS
More
Frag
Retry
Power
Mgmt
More
Data
WEP
2
2
4
1
From
DS
1
Order
bits
1
1
1
1
1
1

## Slide 23: MAC address format
DS: Distribution System
AP: Access Point
DA: Destination Address
SA: Source Address
BSSID: Basic Service Set Identifier
RA: Receiver Address
TA: Transmitter Address

## Slide 24: Special Frames: ACK, RTS, CTS
Acknowledgement
Request To Send
Clear To Send
Frame
Control
Duration
Receiver
Address
Transmitter
Address
CRC
2
2
6
6
4
bytes
Frame
Control
Duration
Receiver
Address
CRC
2
2
6
4
bytes
Frame
Control
Duration
Receiver
Address
CRC
2
2
6
4
bytes
ACK
RTS
CTS

## Slide 25: 802.11 - MAC management
Synchronization
  try to find a LAN, try to stay within a LAN
  timer etc.
Power management
  sleep-mode without missing a message
  periodic sleep, frame buffering, traffic measurements
Association/Reassociation
  integration into a LAN
  roaming, i.e. change networks by changing access points
  scanning, i.e. active search for a network
MIB - Management Information Base
  managing, read, write

## Slide 26: Power management
Idea: switch the transceiver off if not needed
States of a station: sleep and awake
Timing Synchronization Function (TSF)
  stations wake up at the same time
Infrastructure
  Traffic Indication Map (TIM)
    list of unicast receivers transmitted by AP
  Delivery Traffic Indication Map (DTIM)
    list of broadcast/multicast receivers transmitted by AP
Ad-hoc
  Ad-hoc Traffic Indication Map (ATIM)
    announcement of receivers by stations buffering frames
    more complicated - no central AP
    collision of ATIMs possible (scalability?)
APSD (Automatic Power Save Delivery)
  new method in 802.11e replacing above schemes

## Slide 27: END OF WLAN

## Slide 28: Bluetooth
Basic idea
  Universal radio interface for ad-hoc wireless connectivity
  Interconnecting computer and peripherals, handheld devices, PDAs, cell phones – replacement of IrDA
  Embedded in other devices, goal: 5€/device (already < 1€)
  Short range (10 m), low power consumption, license-free 2.45 GHz ISM
  Voice and data transmission, approx. 1 Mbit/s gross data rate
One of the first modules (Ericsson).

## Slide 29
Bluetooth version Max speed Max range
3.0 25 Mbit/s[18] 10 meters (33 ft)
4.0 25 Mbit/s[19] 60 meters (200 ft)
5 50 Mbit/s 240 meters (800 ft)

## Slide 30: Bluetooth
History
  1994: Ericsson (Mattison/Haartsen), “MC-link” project
  Renaming of the project: Bluetooth according to Harald “Blåtand” Gormsen [son of Gorm], King of Denmark in the 10th century
  1998: foundation of Bluetooth SIG, www.bluetooth.org
  1999: erection of a rune stone at Ercisson/Lund ;-)
  2001: first consumer products for mass market, spec. version 1.1 released
  2005: 5 million chips/week
Special Interest Group
  Original founding members: Ericsson, Intel, IBM, Nokia, Toshiba
  Added promoters: 3Com, Agere (was: Lucent), Microsoft, Motorola
  > 10000 members
  Common specification and certification of products
(was: )

## Slide 31: Characteristics
2.4 GHz ISM band, 79 (23) RF channels, 1 MHz carrier spacing
  Channel 0: 2402 MHz … channel 78: 2480 MHz
  G-FSK modulation, 1-100 mW transmit power
FHSS and TDD
  Frequency hopping with 1600 hops/s
  Hopping sequence in a pseudo random fashion, determined by a master
  Time division duplex for send/receive separation
Voice link – SCO (Synchronous Connection Oriented)
  FEC (forward error correction), no retransmission, 64 kbit/s duplex, point-to-point, circuit switched
Data link – ACL (Asynchronous ConnectionLess)
  Asynchronous, fast acknowledge, point-to-multipoint, up to 433.9 kbit/s symmetric or 723.2/57.6 kbit/s asymmetric, packet switched
Topology
  Overlapping piconets (stars) forming a scatternet

## Slide 32: Piconet
Collection of devices connected in an ad hoc fashion
One unit acts as master and the others as slaves for the lifetime of the piconet
Master determines hopping pattern, slaves have to synchronize
Each piconet has a unique hopping pattern
Participation in a piconet = synchronization to hopping sequence
Each piconet has one master and up to 7 simultaneous slaves (> 200 could be parked)
M=Master
S=Slave
P=Parked
SB=Standby
M
S
P
SB
S
S
P
P
SB

## Slide 33: Forming a piconet
All devices in a piconet hop together
  Master gives slaves its clock and device ID
    Hopping pattern: determined by device ID (48 bit, unique worldwide)
    Phase in hopping pattern determined by clock
Addressing
  Active Member Address (AMA, 3 bit)
  Parked Member Address (PMA, 8 bit)
SB
SB
SB
SB
SB
SB
SB
SB
SB
M
S
P
SB
S
S
P
P
SB



















## Slide 34: Scatternet
Linking of multiple co-located piconets through the sharing of common master or slave devices
  Devices can be slave in one piconet and master of another
Communication between piconets
  Devices jumping back and forth between the piconets
M=Master
S=Slave
P=Parked
SB=Standby
M
S
P
SB
S
S
P
P
SB
M
S
S
P
SB
Piconets
(each with a
capacity of
720 kbit/s)

## Slide 35: Bluetooth protocol stack
Radio
Baseband
Link Manager
Control
Host
Controller
Interface
Logical Link Control and Adaptation Protocol (L2CAP)
Audio
TCS BIN
SDP
OBEX
vCal/vCard
IP
NW apps.
TCP/UDP
BNEP
RFCOMM (serial line interface)
AT modem
commands
telephony apps.
audio apps.
mgmnt. apps.
AT: attention sequence
OBEX: object exchange
TCS BIN: telephony control protocol specification – binary
BNEP: Bluetooth network encapsulation protocol
SDP: service discovery protocol
RFCOMM: radio frequency comm.
PPP

## Slide 36: Baseband
Piconet/channel definition
Low-level packet definition
  Access code
    Channel, device access, e.g., derived from master
  Packet header
    1/3-FEC, active member address (broadcast + 7 slaves), link type, alternating bit ARQ/SEQ, checksum
access code
packet header
payload
68(72)
54
0-2745
bits
AM address
type
flow
ARQN
SEQN
HEC
3
4
1
1
1
8
bits
preamble
sync.
(trailer)
4
64
(4)

## Slide 37: Baseband states of a Bluetooth device
standby
inquiry
page
connected
AMA
transmit
AMA
park
PMA
hold
AMA
sniff
AMA
unconnected
connecting
active
low power
Standby: do nothing
Inquire: search for other devices
Page: connect to a specific device
Connected: participate in a piconet
detach
Park: release AMA, get PMA
Sniff: listen periodically, not each slot
Hold: stop ACL, SCO still possible, possibly participate in another piconet

## Slide 38: Bluetooth versions
Bluetooth 1.1
  also IEEE Standard 802.15.1-2002
  initial stable commercial standard
Bluetooth 1.2
  also IEEE Standard 802.15.1-2005
  eSCO (extended SCO): higher, variable bitrates, retransmission for SCO
  AFH (adaptive frequency hopping) to avoid interference
Bluetooth 2.0 + EDR (2004, no more IEEE)
  EDR (enhanced date rate) of 3.0 Mbit/s for ACL and eSCO
  lower power consumption due to shorter duty cycle
Bluetooth 2.1 + EDR (2007)
  better pairing support, e.g. using NFC
  improved security
Bluetooth 3.0 + HS (2009)
  Bluetooth 2.1 + EDR + IEEE 802.11a/g = 54 Mbit/s
Bluetooth 4.0 (2009)
  Low Energy, much faster connection setup

## Slide 39: WPAN: IEEE 802.15 – future developments 3
802.15.4: Low-Rate, Very Low-Power
  Low data rate solution with multi-month to multi-year battery life and very low complexity
  Potential applications are sensors, interactive toys, smart badges, remote controls, and home automation
  Data rates of 20-250 kbit/s, latency down to 15 ms
  Master-Slave or Peer-to-Peer operation
  Up to 254 devices or 64516 simpler nodes
  Support for critical latency devices, such as joysticks
  CSMA/CA channel access (data centric), slotted (beacon) or unslotted
  Automatic network establishment by the PAN coordinator
  Dynamic device addressing, flexible addressing format
  Fully handshaked protocol for transfer reliability
  Power management to ensure low power consumption
  16 channels in the 2.4 GHz ISM band, 10 channels in the 915 MHz US ISM band and one channel in the European 868 MHz band
Basis of the ZigBee technology – www.zigbee.org

## Slide 40: ZigBee
Relation to 802.15.4 similar to Bluetooth / 802.15.1
Pushed by Chipcon (now TI), ember, freescale (Motorola), Honeywell, Mitsubishi, Motorola, Philips, Samsung…
More than 260 members
  about 15 promoters, 133 participants, 111 adopters
  must be member to commercially use ZigBee spec
ZigBee platforms comprise
  IEEE 802.15.4 for layers 1 and 2
  ZigBee protocol stack up to the applications

## Slide 41: WPAN: IEEE 802.15 – future developments 4
802.15.4a:
  Alternative PHY with lower data rate as extension to 802.15.4
  Properties: precise localization (< 1m precision), extremely low power consumption, longer range
  Two PHY alternatives
    UWB (Ultra Wideband): ultra short pulses, communication and localization
    CSS (Chirp Spread Spectrum): communication only
802.15.4b, c, d, e, f, g:
  Extensions, corrections, and clarifications regarding 802.15.4
  Usage of new bands, more flexible security mechanisms
  RFID, smart utility neighborhood (high scalability)
802.15.5: Mesh Networking
  Partial meshes, full meshes
  Range extension, more robustness, longer battery live
802.15.6: Body Area Networks
  Low power networks e.g. for medical or entertainment use
802.15.7: Visible Light Communication
Not all these working groups really create a standard, not all standards will be found in products later …

## Slide 42: Some more IEEE standards for mobile communications
IEEE 802.16: Broadband Wireless Access / WirelessMAN / WiMax
  Wireless distribution system, e.g., for the last mile, alternative to DSL
  75 Mbit/s up to 50 km LOS, up to 10 km NLOS; 2-66 GHz band
  Initial standards without roaming or mobility support
  802.16e adds mobility support, allows for roaming at 150 km/h
IEEE 802.20: Mobile Broadband Wireless Access (MBWA)
  Licensed bands < 3.5 GHz, optimized for IP traffic
  Peak rate > 1 Mbit/s per user
  Different mobility classes up to 250 km/h and ranges up to 15 km
  Relation to 802.16e unclear
IEEE 802.21: Media Independent Handover Interoperability
  Standardize handover between different 802.x and/or non 802 networks
IEEE 802.22: Wireless Regional Area Networks (WRAN)
  Radio-based PHY/MAC for use by license-exempt devices on a non-interfering basis in spectrum that is allocated to the TV Broadcast Service

## Slide 43: RFID – Radio Frequency Identification (1)
Data rate
  Transmission of ID only (e.g., 48 bit, 64kbit, 1 Mbit)
  9.6 – 115 kbit/s
Transmission range
  Passive: up to 3 m
  Active: up to 30-100 m
  Simultaneous detection of up to, e.g., 256 tags, scanning of, e.g., 40 tags/s
Frequency
  125 kHz, 13.56 MHz, 433 MHz, 2.4 GHz, 5.8 GHz and many others
Security
  Application dependent, typ. no crypt. on RFID device
Cost
  Very cheap tags, down to 1€ (passive)
Availability
  Many products, many vendors
Connection set-up time
  Depends on product/medium access scheme (typ. 2 ms per device)
Quality of Service
  none
Manageability
  Very simple, same as serial interface
Special Advantages/Disadvantages
  Advantage: extremely low cost, large experience, high volume available, no power for passive RFIDs needed, large variety of products, relative speeds up to 300 km/h, broad temp. range
  Disadvantage: no QoS, simple denial of service, crowded ISM bands, typ. one-way (activation/ transmission of ID)